## Slide 1: Foundation of computer science
By : Mohamed Agami

## Slide 2: Lecture 4 (part 1)
Motherboard

## Slide 3: Motherboard
Communication tool
Power distribution

## Slide 4
Form factor
Processor Socket
Chipsets
Buses & Slots
1/0 posts
Extra feature

## Slide 5: Form factor
ATX => 12 * 9.6 Inch
Micro-ATX => 9.6 *9.6 Inch
Mini-ITX => 6.7 * 6.7 Inch
Nano-ITX = > 4.7 * 4.7 Inch

## Slide 6: Processor Sockets

## Slide 7: Processor Sockets

## Slide 8: Processor Sockets

## Slide 9: Processor Sockets (Intel)
CPU Sockets Name
Used Processor family
LGA 2066
LGA 1200
LGA 1151
LGA 1150
10th Gen Core
10th Gen Core
9th Gen Core, 8th Gen Core
Four Generation (core i7, core i5 , core i3, Pentium, Celeron)

## Slide 10: Processor Sockets (Intel)
CPU Sockets Name
Used Processor family
LGA 1155
LGA 2011
LGA 1151
Third Generation (core i7, core i5 , core i3, Pentium, Celeron)
Second Generation (core i7, core i5 , core i3, Pentium, Celeron)
Core 2 extreme, Core 2 Quad, Core 2 Dou, Pentium dual core

## Slide 12: Processor Sockets
Pin grad array (PIN)
Land grad array (LIN)

## Slide 13: Processor Sockets (AMD)
CPU Sockets Name
Used Processor family
STRX4
TR4
AM4
FM2+
Ryzen Thread ripper 3000
Ryzen Thread ripper 2000 and 1000
Ryzen 3000, 2000 and 1000
Used with the A10-, A8-, and a6-series of processors
FM2
Used with the trinity line of processors

## Slide 14: Chipsets
Intel
AMD
Manufacturer

## Slide 15
North bridge
South bridge

## Slide 16: Chipsets Intel
North Bridge and South Bridge use a hub architecture
  Intel i800 series of chipsets (start 2006)
  hub using the Accelerated Hub Architecture

## Slide 17
CPU
South Bridge
I/O Controller Hub(ICH)
Front Side Bus(FSB)
North Bridge
Graphics/ Memory Controllers
PCI Link
PCIe Link
PCIe Link
PCIe Slot
PCIe Slot
USB
Sound
64-bit Bus
Drives
PCI Slots

## Slide 19: Chipsets Intel
Nehalem chipsets with the memory controller in the processor.
  The release of the X58 chipset in 2008
  The memory controller was contained in the processor housing
Nehalem chipsets support the Intel LGA1366 socket, the Core i7 processors, and PCI Express Version 2.
First generation

## Slide 20
CPU
South Bridge
I/O Controller Hub(ICH)
Front Side Bus(FSB)
North Bridge
Graphics/ Memory Controllers
PCI Link
PCIe Link
PCIe Link
PCIe Slot
PCIe Slot
USB
Sound
64-bit Bus
Drives
PCI Slots
Nehalem chipsets with the memory controller in the processor.
Graphics Controller
Memory Controller
Quick Path Interconnect(QPI)

## Slide 22: Intel Chipsets
Sandy bridge chipset with the memory and graphic control in the processor
Second generation

## Slide 23
CPU
Platform Controller Hub
(for example, the Intel X79
Express chipset)
Direct Media Interface(DMI)
High Definition Audio
PCIe 2.0
SATA, eSATA
USB 2.0
Ethernet

## Slide 26: IVY bridge chipsets
Use less power
Squeeze more transistors into a smaller space
Perform better than earlier products.
Ivy Bridge chipsets include B75, Q75, Q77, H77, Z75, and Z77.
Third generation

## Slide 27: Haswell Chipset
Forth generation
The fourth generation of Intel chipsets (Intel 8 Series), released in 2013, brought several advancements compared to the previous generation (Intel 7 Series). Here are the most significant developments:
1. Support for Haswell Processors:
2. Improved Power Efficiency:
3. Support for PCIe 3.0:
4. Storage Interface Improvements:
5. Full USB 3.0 Support:
6. Improved Integrated Graphics Performance:
7. Advanced Management and Control Technologies:
8. Support for Thunderbolt:
9. Improved Memory Support:

## Slide 28: Broadwell Chipset
Fifth generation
The fifth generation of Intel chipsets (Intel 9 Series), released in 2014, brought several additions and improvements compared to the previous generation (Intel 8 Series). Here are the key additions:
1Support for Broadwell Processors:
2. Support for M.2 Ports:
3. Support for SATA Express:
4. Improved Integrated Graphics Performance:
5. Improved Power Management:
6. Improved Support for DDR3L Memory:
7. Enhanced Security Features:
8. Improved PCIe Speed:

## Slide 29
Sixth generation
seventh generation
eighth generation
ninth generation
tenth generation
eleventh generation
twelfth generation
thirteenth generation
fourth generation
Skylake intel 100 Series
Kaby Lake intel 200 Series
Coffee Lake intel 300 Series
Coffee Lake Refresh intel 400 Series
Comet Lake intel 400 Series
Rocket Lake intel 500 Series
Alder Lake intel 600 Series
Raptor Lake intel 800 Series
Meteor Lake intel 900 Series
2015
2017
2018
2019
2020
2021
2022
2023
2024
Improved performance and power efficiency, 14nm.
4K support and noticeably faster storage speeds.
Increased cores and enhanced integrated graphics.
More cores and better power efficiency.
Higher processor speeds with PCIe 3.0 support.
PCIe 4.0 support and major graphics improvements.
Hybrid architecture with DDR5 and PCIe 5.0.
Improved performance with more cores and efficiency.
Chiclet architecture for enhanced performance and flexibility.
Year
Generation Name
Name
Important Feature

## Slide 30: AMD Chipset
AMD specialize In Chipset and graphic processor called GPU
  A serial Chipset
  A serial chipset is a series of interconnected chips that manage and coordinate data flow between the CPU, memory, and peripherals in a computer system.
  9 serial Chipset
  Support eight core in processor

## Slide 31
CPU Z

## Slide 32: Tank you